## Slide 1: Interfacing Arduino and Python

## Slide 2: Import
import in python is similar to #include<header_file> in C/C++.
Python modules can get access to code from another module by importing the file/function using import.
import serial
import time
This imports the header file to use the serial functions.
This imports the header file to use time related functions.

## Slide 3: serial.Serial
Syntax:
variable = serial.Serial ('com port', baud rate)
This is to set the baud rate and the com-port number for the serial communication from python code on your pc to Arduino or vice versa.

## Slide 4: .encode()
Syntax:
string_name.encode()
In Python 3.0, strings are stored as Unicode,
For efficient storage of these strings, they are converted into a continuous set of bytes. The process is known as encoding.
There are various encodings present which treats a string differently. The popular encodings being utf-8, ASCII, etc.
NOTE: ASCII, Unicode are different types in which characters are stored.

## Slide 5: time.sleep()
Syntax:
time.sleep(time_in_seconds)
Python's time module has a handy function called sleep().
Essentially, as the name implies, it pauses your Python program.
time.sleep() is the equivalent to the delay() function in Arduino.

## Slide 6: Some additional functions…
The readline method reads one line from the file and returns it as a string.
The string returned by readline will contain the newline character at the end.
Serial_variable.readline()
variable.split(‘character’)
At some point, you may need to break a large string down into smaller chunks, or strings. To do this, you use the split function.
What it does is split or breakup a string and add the data to a list using a defined separator.
Serial_variable.write(string_variable.encode())
The .write() function is used to write a string to the serial.

## Slide 7: Some additional functions in Arduino…
Syntax:
string_variable = Serial.readStringUntil(delimiter);
Delimiter is a condition until which the string is read and the rest of it is left out.
.readStringUntil()
.toint()
Syntax:
int_variable = s1.toInt();
toint() converts the data received into int data type.

## Slide 8: Let’s do some tasks…
Send two integers from python to Arduino. Check the received values and toggle the on-board LED if they are correct.
Send the values back to python serial from Arduino and print the received values in python terminal.

## Slide 9: ASCII chart
End of line sequences
Windows end of line sequence: \r\n
Unix end of line sequence: \n
Mac end of line sequence: \r
ASCII codes and their escape sequences
ASCII Name Description C Escape Sequence
nul null byte \0 (zero)
bel audible bell \a
bs backspace \b
ht horizontal tab \t
nl newline \n
cr carriage return \r